## Slide 1
Exact adaptive DSP packing
for SNN membrane leakage
Mechanism, worked examples and verified trade-offs
Mentor briefing · X · 11 October 2026
Notes: This briefing begins with the neuron operation, then explains runtime packing and its exact decoder. The retained contribution concerns membrane leakage multiplication. Earlier accumulation and overflow candidates appear in the archived conversation, but they are not the measured contribution in this paper.
Source: current manuscript and release evidence index.

## Slide 2
Leakage inside a neuron update
02
Stored membrane U
Leakage
L(U, β)
Charge / current
combination
Threshold
and reset
Weighted input spikes
The teal leakage block is the operation measured in this study
Notes: A leaky integrate-and-fire neuron stores membrane potential U. Leakage decays the previous membrane. Input current charges it, and threshold/reset rules produce the next state and spike. Different source models order these steps differently. The evaluation adapters preserve each original ordering. Only the highlighted leakage primitive has measured FPGA costs.
Sources: paper Sections II and IV, original GLIF/OTTT/TinyImageNet source manifests.

## Slide 3
The exact integer contract
03
L(U, β) = ceil(β × U / 256)
Membrane U: signed16, −32768 to 32767
Coefficient code β: 0 to 256
Example: β = 128 means half leakage
Stored precision stays at 16 bits
Notes: Beta is an integer Q8 coefficient code. Its effective leakage factor is beta/256. Ceiling rounds toward positive infinity, so ceil(-1.5) is -1. The circuit preserves this declared integer operation. Converting an original floating neuron to integer units is separate and can change predictions.
Sources: domain_acceptance_glif_v2.json, paper Equation 1 and model summaries.

## Slide 4
Runtime admission uses actual membranes
04
Condition at this request | Action
Both U values in [−256,255] and β equal | Pack two operations
A membrane is wider or coefficients differ | Execute first as signed16 singleton
Only one operand remains in the frame | Execute that singleton
Adaptation changes issue occupancy
It preserves values, units and stored width
Notes: Admission checks actual values, not only configured operand types. Two small membranes with the same coefficient share a DSP issue. A wide membrane or coefficient mismatch causes an exact singleton. The membrane remains stored at 16 bits. The returned count determines source advancement.
Source: rtl/leak_core16.sv, E5 generate branch and take expression.

## Slide 5
Worked stream and source advancement
05
DSP issue | Input(s), β | Count | Exact output(s)
1 | −3 and 5, β=128 | 2 | −1 and 3
2 | 381, β=78 | 1 | 117
3 | −2 and 7, β=128 | 2 | −1 and 4
The source retains unconsumed operands
Five scalar updates use three DSP issues in this example
Notes: This example uses five ordered operands. The source advances by 2, then 1, then 2, preserving the unconsumed next operand. Results are -1,3,117,-1,4. Three DSP issues replace five scalar issues in this toy. Fixed full-domain packing also uses three here, so this example illustrates mechanics rather than a universal fixed-packing win.
Source: examples/run_examples.py, independently computed integer ceilings.

## Slide 6
A compact multiplicand layout
06
A = (u₀ + 256) + (u₁ << 16)
signed9 u₁
bits24:16
seven zeros
bits15:9
u₀ + 256
bits8:0
One coefficient multiplies both lanes
The products overlap through a possible signed borrow
C = 255 − 256β + 255 × 2¹⁶ supplies exact ceiling offsets
Notes: The lower membrane receives a 256 bias and occupies nine low multiplicand bits. The upper signed membrane begins at bit 16, leaving seven zeros between them. This fits the 25-bit DSP input. The offset C removes the bias after multiplication and supplies both ceiling offsets. A signed borrow can cross the product boundary.
Source: paper Equations 2–4 and leak_core16.sv packed9.

## Slide 7
The low product can borrow one bit
07
P = x + 2¹⁶ y
x = βu₀ + 255 can be negative
The upper field becomes y − n, where n is 0 or 1
Known parity of y recovers that borrow n
Only the rounded output needs correction
Notes: The lower term x can be negative, but its bounded range permits at most one negative borrow. The upper field then equals y minus that borrow. The known odd/even bit of y recovers the borrow with an XOR. This enables a small rounded-result correction instead of general spill reconstruction.
Sources: exhaustive stage3_algebra.json and manuscript decoder proof.

## Slide 8
Negative-borrow example
08
Step | u₀ = −3 | u₁ = 5
β = 128, multiply and add 255 | x = −129 | y = 895
Overlapping packed field | quotient byte 255 | upper field 894
Exact correction | 255 − 256 = −1 | no byte crossing, result 3
Independent integer reference | ceil(−384/256) = −1 | ceil(640/256) = 3
The recovered borrow corrects the signed lower lane exactly
Notes: For membranes -3 and 5 with beta 128, x=-129 and y=895. The lower quotient byte 255 becomes -1 when the borrow correction subtracts 256. The upper field 894 still has quotient 3. The independent integer ceilings agree with both results.
Source: examples/run_examples.py.

## Slide 9
A byte-boundary correction and wide fallback
09
Pair: u₀ = −256, u₁ = 1, β = 1
The borrow turns upper field 256 into 255
Restoring it changes the upper quotient 0 into 1
Exact pair output: (−1, 1)
Wide singleton: U = 381, β = 78 gives 117
Unsafe signed9 wrapping would give −39
Notes: The pair (-256,1) with beta 1 exercises the upper correction boundary. A borrow changes upper field 256 to 255, so restoring it increases the upper quotient from 0 to 1. Separately,381 with beta 78 lies outside signed9. E5 computes 117 in a wide singleton. Unsafe narrowing would produce -39.
Sources: portable examples and GLIF capture unsafe-wrap check.

## Slide 10
Counted core and external source
10
External source
and zero filter
Range + β tests
Pair / singleton
One DSP48E1
registered result
Borrow recovery
Quotient correction
Ordered signed16
results and count
consume 1 or 2 after acceptance
Two advancing edges without stalls. Source memory and complete-neuron scheduling remain external
Notes: The measured core includes range tests, coefficient equality, operand selection, the DSP, quotient correction and the elastic interface. Its source queue, operand memory and common zero filter remain external. Core latency is two advancing edges without stalls. Neither source integration nor complete-neuron latency has been measured.
Sources: hardware/route12_e5_a0/hardware.json, rtl/timing16.sv, manuscript Figure 1.

## Slide 11
Strong controls execute the same operation
11
Control | Purpose
E1 fixed split, one DSP | Fullsigned16 pairs with exact fabric high parts
E3 / E4 scalar DSP | Two DSP pair / one DSP singleton
E7 general LUT pair | Exact full domain, zero DSP
E6 half-leakage shift | Exact zero DSP control for β=128
E9 shared GLIF constants | Zero DSP pair supporting all 33 trained codes
Same operation, same 12 ns route fixture, same operands within each energy comparison
Notes: All general controls compute the same signed16 leakage contract. E1 retains full-domain pairs using DSP residue products and fabric high parts. E3 uses two scalar DSPs, E4 one, and E7 uses general LUT arithmetic. E6 is legal only for half leakage. E9 supports the 33 trained GLIF coefficient codes using shared add/sub logic. These are matched constructed primitives rather than reproduced FireFly accelerators.
Sources: route and energy manifests.

## Slide 12
Exactness and protocol validation
12
67,371,008 exhaustive narrow pair cases
16,842,752 full-domain scalar / split cases
Stalled RTL checks verify order and held outputs
All 33 GLIF coefficients pass exhaustive new-control RTL
Zero differences from the declared integer oracle
Notes: Exhaustive arithmetic checks cover every stated narrow pair and full-domain scalar/split case. Native RTL checks also verify consumption, ordering and held outputs under stalls. The added GLIF constant control passes all 65536 signed16 values for each of its 33 coefficients and the entire representative workload, both stalled and unstalled.
Source: stage3_algebra.json, domain_acceptance_glif_v2.json, native receipts, E9 independent_readiness_native_only_a0.json.

## Slide 13
Public neuron model benchmarks
13
Model / dataset | Validation scope | Packing result
GLIF ResNet18 / CIFAR10 / T2 | 10k conversion,64 packed | All integer states/spikes/logits agree
OTTT VGG11 / CIFAR10 / T6 | 10k packed feedback | All integer updates agree
BNTT-style VGG11 / TinyImageNet / T30 | Predeclared64-image subset | All integer states/spikes/logits agree
FP32-to-integer conversion changes some predictions
Packing adds no further differences in these checks
Notes: GLIF uses a full 10000-image conversion reference but 64-image packed feedback. OTTT uses full 10000-image packed feedback. The independent TinyImageNet model uses a predeclared 64-image subset. Exact agreement refers to packed versus scalar integer states/spikes/logits. Floating-to-integer conversion changes some network predictions, and those changes are reported separately.
Sources: stage2_acceptance, stage3_results, benchmark_acceptance, bntt_acceptance.

## Slide 14
Selected core resource trade-offs
14
Chart: Core LUTs
| E4 scalar | E3 pair | E5 adaptive | E1 fixed | E7 LUT | E9 constants
Core LUTs | 13 | 35 | 62 | 202 | 330 | 375
E5: 62 LUT / 44 FF / 1 DSP
E1: 202 LUT / 79 FF / 1 DSP
E3 uses 2 DSP. E7 and E9 use 0 DSP. Shared 94 fixture FFs excluded from core area
Notes: Bars show core LUT counts at selected matched 12 ns routes. The common 94 fixture FFs are excluded from these core resources. E5 and E1 both use one DSP. E3 uses two DSPs. E7 and E9 use zero DSPs. E9 is one shared implementation covering all trained GLIF coefficient codes, not a lower bound for every possible constant design.
Sources: selected hardware.json receipts and E9 hardware/route12_a0/hardware.json.

## Slide 15
Representative GLIF dynamic energy
15
Chart: pJ per scalar operand
| E3 pair | E5 adaptive | E4 scalar | E1 fixed | E7 LUT | E9 constants
pJ per scalar operand | 21.371 | 21.599 | 24.648 | 55.308 | 124.198 | 96.758
E5 saves 60.95% against E1
E3 remains near energy parity using two DSPs
Estimated fixture dynamic energy at 25 °C. Common 94 fixture FFs included
Notes: Bars show representative GLIF fixture dynamic energy per scalar operand. Every compared engine receives the same declared operands. E5 uses 21.599 pJ, E1 fixed split 55.308 pJ, one-DSP scalar 24.648 pJ, two-DSP scalar 21.371 pJ and general LUT 124.198 pJ. The independently audited GLIF constant control uses 96.758 pJ. Energy excludes chip static power, operand memory and whole-neuron integration.
Sources: explicit selected power map, physical audits, E9 independent_readiness_full_a0.json.

## Slide 16
Pairing opportunity depends on the workload
16
Chart: Extra issues versus E1 (%)
| GLIF 64 | OTTT 10k | TinyImageNet 64
Extra issues versus E1 (%) | 1.0836 | 54.9444 | 27.0303
GLIF: 1.852 useful results per issue
Wider membranes make fixed full-domain pairs more attractive
Notes: These values show E5 extra leakage issues relative to fixed E1. GLIF small membranes allow nearly full pair occupancy, whereas the wider OTTT and TinyImageNet streams cause many singletons. Leakage issue counts do not establish complete-network runtime or burst latency.
Sources: stream profiles and Table 2.

## Slide 17
Constant leakage defines an important negative case
17
Chart: OTTT representative pJ/scalar
| OTTT half shift | OTTT E5 | OTTT E1
OTTT representative pJ/scalar | 13.658 | 26.58 | 36.808
For β=128, exact shifting wins
For β=253, an exact shift/add identity also exists
The β=253 circuit and energy have not been measured
Notes: Half leakage has a cheap exact shift control. It beats E5 on OTTT energy. The TinyImageNet coefficient 253 also has an exact shift/add identity, although its hardware and energy remain unmeasured. This bounds the useful conditions for a general DSP primitive.
Sources: OTTT representative accepted closure and BNTT exact constant check.

## Slide 18
Specific novelty and established ingredients
18
Established: value-based packing and signed correction
Specific mechanism: compact exact leakage quotient recovery
Integrated contribution: actual-U admission with wide fallback
Evidence: measured same-operation trade-offs and model exactness
A new integrated mechanism can contribute
A proven worldwide first-ever claim is unnecessary here
Notes: Operation packing, actual-value narrowness detection and signed correction have established ancestry. The specific contribution is the compact exact rounded-leakage decoder integrated with actual-membrane admission and a wide singleton contract. The available review has not identified an equivalent implementation, but three original full methods remain unavailable. A worldwide first-ever claim is not established.
Source: paper related work and readiness review.

## Slide 19
Paper recommendation and remaining limits
19
Proceed with a focused leakage-primitive submission
Keep the exact decoder and membrane admission as one contribution
Report positive GLIF trade-offs and constant-leakage negative cases
Keep external integration and board-level claims outside the evidence
Readiness supports submission preparation
Reviewers determine novelty significance and acceptance
Notes: The evidence supports preparation of a focused circuit submission. The paper should report exactness, measured resources, conditional energy benefits and negative cases. It should avoid claims about a complete accelerator, board energy, improved accuracy or universal burst latency. Reviewers determine the significance of the contribution and acceptance.
Source: current paper and readiness report.

## Slide 20
Mentor handoff and reproduction
20
github.com/riteshdasari/membrane-leakage-packing
README and worked integer examples
IEEE paper source and editable diagrams in these slides
Full user-facing chat export and archived research code
Evidence manifest with accepted results and failed attempts
OpenAI Codex assisted prototyping, validation, analysis, drafting and slides. Author placeholder: X
Notes: The public repository packages the paper, slides, executable examples, research-authored source archive, lightweight evidence receipts and user-facing conversation export. Large weights, datasets and vendor artifacts remain external. The reading guide helps the mentor assess the final mechanism without following every discarded experiment.
Source: README and docs/REPRODUCIBILITY.md. AI disclosure: OpenAI Codex assisted RTL, software, evidence review, drafting and slides. X is the author placeholder.

## Slide 21
Appendix: exact decoder equations
21
r = (LSB(β) AND LSB(u₁)) XOR 1
n = P₁₆ XOR r
L₀ = unsigned(P[15:8]) − 256n
L₁ = signed9(P[32:24]) + (n AND P[23:16] = 255)
P[i:j] selects inclusive bits i through j
LSB denotes the least significant bit (odd/even parity)
Notes: The lower quotient takes product bits 15:8 as an unsigned byte and subtracts 256 times the recovered borrow. The upper quotient interprets bits 32:24 as a signed9 value and adds 1 only if the borrow exists and product bits 23:16 are 255. Bits denote positions in the two-complement product. The parity reference needs only coefficient bit 0 and upper membrane bit 0. Source: manuscript Equations 5–6 and examples/leakage_reference.py.

## Slide 22
Appendix: the exact fixed split reference
22
U = 256h + q, with 0 ≤ q ≤ 255
L = βh + ceil(βq / 256)
Input | High part in fabric | Residue in DSP | Exact sum
U=381, β=78 | 78 × 1 = 78 | ceil(78 × 125 / 256) = 39 | 117
U=−3, β=128 | 128 × (−1) = −128 | ceil(128 × 253 / 256) = 127 | −1
Fixed E1 keeps full-domain pair occupancy and pays for the high-part fabric
Notes: Fixed E1 writes U = 256h + q, where q lies between 0 and 255 and h = floor(U/256). It computes beta times h in fabric and packed beta times q in the DSP. Since beta times h is an integer, ceil(beta U/256) = beta h + ceil(beta q/256). For U = 381 and beta = 78, h = 1 and q = 125, giving 78 + 39 = 117. For U = -3 and beta = 128, h = -1 and q = 253, giving -128 + 127 = -1. It preserves full-domain pair occupancy but pays for the high-part arithmetic. Source: manuscript fixed control equation and leak_core16.sv E1 split branch.